## Slide 1: Wireless Carbon Nanofiber Aggregate Sensor System for Real-Time Water Level Monitoring and Flood Warning
Y.L. Mo, Yuhua Chen , Jinghong Chen – University of Houston
T.G. Cleveland Texas Tech University

## Slide 2: Application Concept
(1) Sensor embedded into material.
(2) Microprocessor sends signal to warning display

## Slide 3: Sensor(s)
Embedded Sensor
  Monitors health of structural element, not just water depth
  Depends on water to compress material to generate a low magnitude stress signal
Contact Sensor
  Depends on water to complete a circuit
  Measures water only
  Image shows sensor, and microprocessors

## Slide 4: Status
Contact Sensor
  Proven technology
  System integration and fabrication of self-calibrating sensor ladders
  Power management is an issue -- as pictured the device uses a lot of power – the microprocessor has to sleep and awake for reasonable run time on battery supply
  What is desirable failure mode behavoir (to program into the microprocessor)

## Slide 5: Status
Embedded Sensor
  Sensitivity – Needs to perform in the “blue” region for water detection
Sensitivity is frequency related

## Slide 6: On-Going Path
Contact sensor considered as a state-of-practice level technology
Embedded sensor to be developed to produce information on par with contact sensor